## Slide 1: Details for Drawing Packages (Content and GD&T)
Special Topic Lecture
February 26, 2018
UTSA

## Slide 2: Geometric Dimensioning and Tolerancing (enough to get you to a working level, but not an expert)
What and Why?
Datum Reference
Feature Control Frame
Material Conditions
Locational Tolerances
Profile/runout/orientation/form tol.
Conversion (positional to coordinate)

## Slide 3: History
Introduced by Stanly Parker (Scotland, 1930’s)
Use proliferated during WW II because the need of high production quantities from numerous shops
Designer could discuss with manufacturing personnel what features were to be contacted to establish centerlines that were used on drawings to locate features such as holes and keyways, but a system was needed to get it on paper!
Greatly reduced the cost of “make overs” or need for in shop modifications

## Slide 4: What is GD & T ?
It is a compilation of symbols and rules that effectively describe and control
dimensioning and tolerancing for all
drawings. It is documented in ASME
Y14.5 (Y14.8 for castings and forgings)

## Slide 5
Simple and efficient method for describing tolerancing mandated
by the designer of the part
Eliminates ambiguities as to what datum features are to be contacted
to establish the datum planes and/or datum axis that are use for
locating features (all inspectors get the same results)
Simplifies inspection because hard gages can be utilized and simplifies
Inspection for production quantities
Forces the designer to totally consider function, manufacturing
process,and inspection methods. The result is larger tolerances
that guarantee function, but reduce manufacturing and inspection costs.
Why use GD & T ?

## Slide 6
Coordinate Measurement Machine - CMM
Sensitive Contact Probe
Stable Base
3-Axis Control

## Slide 7
Fixed and Moving Bridge

## Slide 8
https://www.youtube.com/watch?v=umtgJNiWyEw

## Slide 9
“Old” Drawing with GD&T*
* Geometric Dimensioning and Tolerancing

## Slide 10
“New” Drawing with GD&T*
* Geometric Dimensioning and Tolerancing

## Slide 12
Questions Answered with “New”

## Slide 13
Primary, Secondary, and Tertiary
Datum Planes

## Slide 15
Special Fixtures such as highly
Polished stone or stable metals

## Slide 17: Feature Control Frame

## Slide 18
Taylor Principle
(envelope principle)
If you dimension like this,
how is it interpreted?

## Slide 19: Maximum Material Condition
Refers to the envelop size or mating size at the maximum material size (largest external dimensions and smallest internal conditions).
This is the “part material state” to which tolerancing will be applied.

## Slide 21: Least Material Condition
Refers to the envelop size or mating size at the minimum material size (smallest external dimensions and largest internal conditions).
This is the “part material state” to which tolerancing will be applied.

## Slide 26
Positional Tolerance for Holes

## Slide 28
Positional Tolerance for Keyway

## Slide 32
Run Out Tolerances

## Slide 33
FIM=full indicator movement
[RFS] (regardless of feature size)
(multiple measurements)

## Slide 34
These are left in place for full rotation

## Slide 36
Perpendicularity of a feature of size axis
at MMC with datum feature of size at MMC

## Slide 48: Good Dimensioning (Conventional Practice)
The keys to good dimensioning are:
  Choice of dimensions
  Placement of dimensions
  Technique of dimensioning
  Specifying dimension tolerances

## Slide 49: Choice of Dimensions
The dimensions you specify define how the object is manufactured:
  Dimension first for function and then review seeking improvements for production/manufacturing purposes such as manufacturability, inspection, etc.
Do not give superfluous dimensions
  Only those dimensions that are needed to manufacture and inspect the object are to be included on the drawing
  Each dimension should appear only once; do not repeat dimensions in different views.

## Slide 50: Placement of Dimensions
Follow accepted standards so that dimensions are legible, easy to find, and easy to interpret.
The spacing of dimensions lines must be uniform throughout the drawing.

## Slide 51: Placement of Dimensions
Do’s & Don’t’s
  Avoid dimensions on the object itself
  Avoid dimensioning to hidden lines
  Do group dimensions around a central view

## Slide 52: Placement of Dimensions
Conventional practice for placement of dimension and extension lines.

## Slide 53: Technique of Dimensioning
Follow accepted standards & practices for the appearance of lines, spacing of dimension lines, size of arrowheads, etc. so that others may correctly interpret your drawing.

## Slide 54: Lines Used in Dimensioning
A dimension line is a thin, dark, solid line terminated by arrowheads that indicate the direction and extent of a dimension.

## Slide 55: Lines Used in Dimensioning
An extension line is a thin, dark, solid line that extends from a point on the drawing to its associated dimension line.
  A gap of ~1.5 mm should be left between the extension line and the point on the part.

## Slide 56: Lines Used in Dimensioning
A center line is a thin, dark, solid line that alternates long and short dashes to locate holes and other symmetrical features.

## Slide 57: Lines Used in Dimensioning
Arrowheads are used to indicate the extent of a dimension. They should be uniform in size & style throughout the drawing.

## Slide 58: Lines Used in Dimensioning
An leader is a thin, solid line directing attention to a note or dimension. A leader starts with an arrow or dot:
  Use an arrow when the leader can point to a specific line in the drawing such as the edge of a surface
  Use a dot when the leader is locating a feature within the outline of the part

## Slide 59: Dimension Tolerances
A tolerance is required for every dimension on a drawing. Definition: a tolerance is the total amount that the feature on the actual part is allowed to vary from what is specified by the dimension.
  A general tolerance applicable to most dimensions can be specified in the title block.
    Example: “All tolerances +/- 0.01 inches unless otherwise noted”.
  A tolerance for a particular dimension may be specified by limit dimensions or plus and minus dimensions.
    Example: “1.500 +/-.003” or “1.252/1.248”

## Slide 60: Dimension Tolerances: Examples

## Slide 61: Dimension Tolerances
The purpose of dimension tolerances:
  Allows a range of acceptable variability on the dimensions of a part
  Assures that parts interchanged between assemblies will fit properly
  Allowing parts be manufactured to prescribed tolerances rather than exact dimensions permits efficient and economical manufacturing. In general: high precision means high cost!

## Slide 62: Dimension Tolerances
Tolerance stacking is to be avoided by dimensioning with respect to a datum.

## Slide 63: Do’s & Don’ts of Dimensioning
Do not trust the automatic creation & placement of dimensions done for you by CAD software.
  Each dimension should be given clearly so that it can be interpreted only one way
  Dimensions should not be duplicated
  Dimensions should be given so that the machinist will not have to calculate, scale, or assume any dimensions.

## Slide 64: Dimensioning: Examples

## Slide 65: Dimensioning: Examples

## Slide 66: Dimensioning: Examples

## Slide 67: Dimensioning: Examples

## Slide 68: Dimensioning: Examples

## Slide 69: Dimensioning: Examples

## Slide 70: Dimensioning: Examples

## Slide 71: Dimensioning: Examples

## Slide 72: Dimensioning: Examples

## Slide 73: Dimensioning: Examples

## Slide 74: Dimensioning: A real drawing